Fruit Exploder
(“Lil McMaster Disaster)
John McMaster JohnDMcMaster@gmail.com

---
What
- High voltage capacitor stores energy
- High voltage switch closes, completing circuit
- Electrode focuses plasma => explosion
- There is no “Why” slide

---
How much energy?
- E = 1/2 C V^2
- E = 1/2 * 0.25e-6 * 80e3^2 = 800 J
  - C = 0.25e-6
  - V = 80e3
- Loud! Run at half voltage
- E = 1/2 * 0.25e-6 * 40e3^2 = 200 J

---
First test

---
Final schematic

---
Obtaining HV transformer

---
Obtaining HV transformer

---
Transformer test: box

---
Transformer test: sparks!

---
HV rectifier first cut

---
Prototype: PS

---
Prototype: HV switch

---
Prototype: capacitor (1/2)

---
Prototype: capacitor (2/2)

---
Improving HV box
- Add second transformer half => full voltage
- Seal so oil doesn't splash out
- Add electrical interface
- Fix components in place

---
PS: pre-oil

---
PS: post oil

---
PS: assembled

---
PS: polishing

---
Detonator: improvements
- Problem: compressor heavy, no reset
- Idea: bicycle pump like ACME TNT detonator

---
Detonator: planning

---
Detonator: reset

---
Detonator: assembling

---
Detonator: complete

---
Improved safety gap

---
Improved HV switch

---
Improved meter

---
Improved shield

---
Final setup

---
Future work

---
Future work
Plasma cannon on SC1 siege tank

---
Thanks for listening!
- Questions? Interested?
  - JohnDMcMaster@gmail.com